## Slide 1
Design and Simulation of a Physical Even and Odd Parity Generator Using XOR Gates
Digital Design & Computer Architecture – PBL Project
Team Members
M. SUJAN
ACHSAH .P
A. SAMANVITHA
S. MOKSHITH
Y. RESHMA
Academic Year
2024–2025

## Slide 2
Introduction to Combinational Logic
Combinational Circuit
Output depends only on current inputs — no memory of previous states.
No Memory Element
Unlike sequential circuits, combinational logic does not store any previous input states.
Building Blocks
Constructed from fundamental logic gates: AND, OR, XOR, NOT, and their combinations.
Parity Generator
A simple, practical, and elegant example of combinational logic in action.
Core Principle: Inputs → Combinational Logic → Output

## Slide 3
The XOR Gate
Exclusive OR (XOR) Gate
Boolean Expression: Y = A ⊕ B
Logic: Output is 1 when inputs are different; output is 0 when inputs are the same.
Key Property: Perfectly suited for parity generation — naturally counts the number of 1s.
A | B | Y = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 4
What is Parity?
Parity Defined
Parity is a simple and widely-used error-detection technique in digital communication. A parity bit is an extra bit appended to binary data to ensure the total count of 1s is either even or odd.
Example: Data = 101 (two 1s)
Even parity bit = 0 → total: 2 ones (even ✓)
Odd parity bit = 1 → total: 3 ones (odd ✓)
Even Parity
Total number of 1s (including parity bit) must be even.
Odd Parity
Total number of 1s (including parity bit) must be odd.

## Slide 5
Even Parity Generator (3-bit)
Boolean Expression
Pₑ = A ⊕ B ⊕ C
The XOR of all input bits generates the even-parity bit. Output is 1 when an odd number of inputs are 1, ensuring the total count of 1s (data + parity) remains even.
Two cascaded 2-input XOR gates implement this expression: first XOR(A,B), then XOR(result, C).
Truth Table — Even Parity
A | B | C | Pₑ
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 6
Odd Parity Generator (3-bit)
Boolean Expression
Pₒ = NOT(A ⊕ B ⊕ C)
The XOR of all input bits is inverted to generate the odd-parity bit. Output is 1 when an even number of inputs are 1, ensuring the total count of 1s (data + parity) remains odd.
Two cascaded 2-input XOR gates implement the core expression: first XOR(A, B), then XOR(result, C), followed by a NOT gate.
Truth Table — Odd Parity
A | B | C | Pₒ
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 7
Circuit Design & Implementation Flow
Circuit Diagram
Logic Gates
Boolean Expression
Truth Table
Specification
Specification
Design a 3-bit even/odd parity generator using XOR and NOT gates.
Boolean Expressions
Pₑ = A ⊕ B ⊕ C | Pₒ = NOT(A ⊕ B ⊕ C)
Verification
Simulate all 8 input combinations and confirm outputs match the truth table.

## Slide 8
Simulation & Verification
Simulation Setup
Tool: Logisim or equivalent digital circuit simulator
Components: XOR gates, NOT gate, input switches, output LEDs
Testing: Apply all 8 input combinations (000 → 111)
Verification: Confirm outputs match truth table for both parities
Why Simulate First?
Verify logic before physical construction
Test all edge cases quickly and safely
Identify and fix design errors early
Visualize real-time circuit behavior

## Slide 9
Physical Implementation
IC 7486 — XOR Gate
Quad 2-input XOR gate. Two gates cascade to implement Pₑ = A ⊕ B ⊕ C.
IC 7404 — NOT Gate
Hex inverter. Complements the XOR output to produce Pₒ (odd parity).
Breadboard & Wiring
Circuit assembled on breadboard with toggle switches for inputs A, B, C and LEDs for output indication.
Power & Testing
+5V DC supply. Apply all 8 combinations and verify LED outputs against the truth table.
Process: Simulation → Breadboard Layout → Physical Wiring → Testing & Verification

## Slide 10
Results, Applications & Conclusion
✓ Project Results
Designed 3-bit even and odd parity generators
Used XOR (7486) and NOT (7404) gates as core logic elements
Verified design using comprehensive 8-row truth tables
Successfully simulated the circuit in Logisim
Demonstrated combinational logic bridging theory and practice
Real-World Applications
Digital communication & data transmission
Error detection in memory systems (RAM, ROM)
Computer networks & communication protocols
Data storage & integrity verification
Thank you to our audience for your time and attention, to our instructors for their guidance and support, and to our team members for their dedication and collaboration throughout this project. We truly appreciate everyone who helped make this work possible.
Thank You